## Slide 1: Blood Glucose Monitoring
March 2023
www.qsource.org

## Slide 2: Preparation Prior To Procedure
Review resident chart (medical history, medications).
Assess resident for signs and symptoms of hypoglycemia or hyperglycemia.
Check physician order for routine and on-going blood glucose monitoring (often done prior to mealtime and antidiabetic medication administration).

## Slide 3: Gather Supplies
Hand sanitizer
Nonsterile gloves
Alcohol swab
Gauze or cotton ball
Reagent strips
Glucometer (ensure you follow manufacturer instructions and facility policy and procedure)

## Slide 4: Perform Safety Steps
Perform hand hygiene.
Check resident room for any precautions.
Introduce yourself, explain the procedure, and allow for any questions.
Confirm resident identification.
Ensure you provide privacy.

## Slide 5: Performing The Blood Glucose Check
Ask resident to wash their hands.
Use alcohol swab to cleanse the puncture site.
Apply nonsterile gloves.
Remove reagent strip from container and reseal the cap (do not touch the test area of the reagent strip).
Turn on glucometer. Place reagent strip in glucometer (ensure it is on a clean and dry surface - e.g., paper towel, with test area facing up, always follow manufacturer instructions). Do not place the reagent strip or glucometer directly on bed or chair.
Perform skin puncture with lancet. Transfer drop of blood to the reagent strip.

## Slide 6: Performing The Blood Glucose Check
Apply pressure to puncture site with gauze or cotton ball.
Read results on glucometer display. Review results with resident (after procedure document and make notifications as needed per your facility policy).
Turn off glucometer and dispose of supplies. Immediately place sharps in sharps safety disposal box.
Remove gloves and perform hand hygiene.

## Slide 7: Cleaning The Glucometer
Perform hand hygiene and put gloves on before cleaning contaminated glucometer.
Place glucometer on clean, protective barrier until disinfection is complete (e.g., paper towel). Do not place contaminated glucometer on any surface without a clean, protective barrier.
Follow manufacturer instructions for cleaning and disinfecting the device.
Disinfect glucometer with an EPA approved wipe. Alcohol wipes are not appropriate for cleaning/disinfecting a glucometer.

## Slide 8: Cleaning the Glucometer (cont.)
During disinfection, ensure contact time is met per manufacturer recommendation.
After cleaning the glucometer, remove gloves and perform hand hygiene.
If setting a timer or stopwatch to ensure accuracy of contact time, make sure to perform hand hygiene after touching the timer or stopwatch.
Always know and follow your facility specific policies and procedures.

## Slide 9: Contact Information
Teresa Hostettler | thostettler@qsource.org | (317) 559-6543
Candace Lord | clord@qsource.org | (317) 829-0143
Nedra Bridgewaters | nbridgewaters@qsource.org | (317) 678-9088
Angeleta Hendrickson | ahendrickson@qsource.org | (317) 735-3551
Marilyn Farran | mfarran@qsource.org | (317) 559-6519
Jerrie Yost | jyost@qsource.org | (317) 868-5057
Sarah Wall | swall@qsource.org | 317-868-5084

## Slide 10: Thank You
www.qsource.org
This material was prepared by Qsource, a/an Network of Quality Improvement and Innovation Contractors under contract with the Centers for Medicare & Medicaid Services (CMS), an agency of the U.S. Department of Health and Human Services (HHS). Views expressed in this document do not necessarily reflect the official views or policy of CMS or HHS, and any reference to a specific product or entity herein does not constitute endorsement of that product or entity by CMS or HHS. 23.QIO.CLIN6.03.019